## Slide 1
Mahesh Awati
Department of Electronics and Communication Engg.
Embedded System Design Concepts
A simple approach

## Slide 2
Objective:
EMBEDDED SYSTEM DESIGN
A simple hands-on approach
To meet the Job description of various companies working in embedded domain
Embedded System Design Concepts - A simple approach

## Slide 3
Electronics ( Electronic Principles, Digital Electronics)
Microprocessor/ Microcontroller
Protocols – UART,SPI,CAN and so on
Programming (Minimum C )
How to get a JOB in EMBEDDED DOMAIN?
EMBEDDED SYSTEM DESIGN
A simple hands-on approach
Embedded System Design Concepts - A simple approach

## Slide 4
Introduction to Embedded System
Embedded System Design Concepts - A simple approach
Mahesh Awati
Department of Electronics and Communication Engineering

## Slide 5
An embedded system is an electronic/electro-mechanical system designed to perform a specific function involving a combination of both hardware and firmware (software).
Electronic/Electro-Mechanic
A Specific Function
Combination of Hardware & Firmware.
Respond, monitor, control external environment using sensors and actuators.
What is an embedded system ?
“A Combination of hardware (electro/electro-mechanical ) & Software performing a specific task without human intervention”
Embedded System Design Concepts - A simple approach

## Slide 6
System Core (ASIC/SoC/FPGA /DSP/MP/MCU)
Memory
Other Supporting Integrated Circuits & Subsystems
(Human Interface, Diagnostic tools, Heat Management)
O/P PORT
I/P PORT
Embedded Firmware Embedded to perform a Particular Task
Communication Interface (UART,USB,DB9,Ethernet)
Diagnostic Unit
Fault Detection and correction
Self Test Tools
Elements of Embedded System
Digital Sensors
Analog Sensors
ADC
LED,BUZZER,RELAY,Display Devices like LCD
DAC
Embedded System Design Concepts - A simple approach

## Slide 7
Embedded systems are domain and application specific and are built around a central core.
The core of the embedded system falls into any of the following categories:
  General purpose and Domain specific processor.
      General Purpose Processors: Microprocessors (GPP)
      Domain Specific - Application Specific Instruction Processors(ASIP) : They have processor with architecture and instruction set optimized to specific-domain/application requirements
          Microcontrollers(industrial)
          Digital signal processors(DSP) ,Networking Processors.
          Automotive and telecom
          Application Specific Integrated Circuits (ASIC)
          Programmable logic devices (PLD’s):CPLDs & FPGA
          SoC (Multiprocessor cores (ARM +DSP + Peripherals))
System Core of Embedded System
Embedded System Design Concepts - A simple approach

## Slide 8
A Processing Unit - Microprocessor
Register File
Register Files are set of registers which are used to store
Data
Address of Memory/IO Devices
Intermediate Results and so on
Control Unit
Control Unit – It is used generate the required control signals based on instructions decoded.
ALU – Arithmetic and Logical Unit
Arithmetic Operation like
Addition
Subtraction
Multiplication
Division
Logical Operation like
AND,OR,XOR ……so on
Arithmetic and Logical (ALU) Unit
General purpose System Core – Basic blocks
Embedded System Design Concepts - A simple approach

## Slide 9
A Microprocessor based system
Memory
(ROM and RAM)
IO PORT
IO PORT
INPUT DEVICE
OUTPUT DEVICE
ROM
RAM
A General purpose Processor can be called as system iff we interface
Memory – ROM and RAM
Input Device through Input Port and
Output device through output port.
Other interfaces depending on system requirements like – Timer/Counter, PWM, ADC,DAC and Serial communication protocols and so on.
Embedded System Design Concepts - A simple approach

## Slide 10
A Microcontroller
Domain Specific - Application Specific System Core – Basic blocks
CPU/ALU
ROM
RAM
Clock Generator
I/O PORTs
ADC
DAC
Timer/ Counter
Communication Protocols (UART,SPI and so on)
PWM
Embedded System Design Concepts - A simple approach

## Slide 11
ARM Cortex M3 as System Core
Embedded System Design Concepts - A simple approach

## Slide 12
ARM Cortex M3 as System Core
What is ARM Cortex M3?
  Advanced RISC Machine.
  Harvard Architecture.
  M –Microcontroller Series/ version.
  LPC – Low Power Controller.
Embedded System Design Concepts - A simple approach

## Slide 13
Features of LPC1768
General purpose 32-bit microprocessor.
Operating frequencies of up to 100 to 120MHz CPU frequency.
Built-in Nested Vectored Interrupt Controller (NVIC).
Up to 512 kB on-chip flash program memory, up to 64 kB of data memory.
Eight channel General Purpose DMA controller (GPDMA).
Peripherals:
  8 Channel 12 bit ADC
  10 bit DAC.
  Timer/ Counter -04.
  PWM - 06.
  GPIO -70 programmable pins
  RTC.
Serial Protocols: UART – 04, Serial Peripheral Interface (SPI) – 02, Inter Integrated Circuit ( I2C ) – 03, Ethernet -01, Controller Area Network (CAN) – 02, USB - 01.
Embedded System Design Concepts - A simple approach

## Slide 14
Header File
LPC17xx.h
The Name of Registers, Data structures that we use are defined in LPC17xx.h header file.
LPC17xx.h header is based on CMSIS(Cortex Microcontroller System Interface Standard) developed by ARM
As per the CMSIS convention, the different registers are grouped into different structures
LPC_GPIOx is defined as a pointer to this structure in LPC17xx.h header.
Example: all registers for Port 0 are grouped into structure defined as LPC_GPIO0.
Embedded System Design Concepts - A simple approach

## Slide 15
Low Power, Pin function, mode, clock generation
Embedded System Design Concepts - A simple approach
Mahesh Awati
Department of Electronics and Communication Engineering

## Slide 16
The Power , Pin function , Pin mode , peripheral clock are need to be done for any on-chip peripheral to be used
  Power Control for Peripheral : PCONP
  Pin Function Selection : PINSEL
  Peripheral Clock Select : PCLKSEL
  Pin Mode Selection : PINMODE
System Control Register – Power, Pin function, mode, clock
All these are member of LPC_SC (system control) structure
Embedded System Design Concepts - A simple approach

## Slide 17: Power Control for peripherals (PCONP)
The PCONP register allows turning off selected peripheral functions for the purpose of saving power.
This is accomplished by gating off the clock source to the specified peripheral blocks.
Some peripherals, particularly those that include analog functions, may consume power that is not clock dependent. These peripherals may contain a separate disable control that turns off additional circuitry to reduce power.
System Control Register – Power, Pin function, mode, clock
On Reset PCONP= 0x042887DE = 0000 0010 1000 1000 0111 1101 1110 b
Embedded System Design Concepts - A simple approach

## Slide 18: PINSEL Register – To choose Multifunctions of a PIN
4:1 MUX
Primary
1st Alternate
2nd Alternate
3rd Alternate
Select 1 Select 0
P0.0
System Control Register – Power, Pin function, mode, clock
Why PINs are configured to perform Multifunction ?
PINSEL Register bits for pin | Functions
00 | Primary (default) function, typically GPIO port
01 | First alternate function
10 | Second alternate function
11 | Third alternate function
Embedded System Design Concepts - A simple approach

## Slide 19: PINSEL Register – To choose Multifunctions of a PIN
System Control Register – Power, Pin function, mode, clock
Each PIN does 4 functions with 3 alternate and 1 primary function as GPIO.
Few alternate functions can be done by multiple pins.
Embedded System Design Concepts - A simple approach

## Slide 20: PINSEL Register – To choose Multifunctions of a PIN
System Control Register – Power, Pin function, mode, clock
Embedded System Design Concepts - A simple approach

## Slide 21: PINSEL Register – To choose Multifunctions of a PIN
PORT P0 [31:16] | PORT P0 [15:0]
PINSEL1[31:0] | PINSEL0[31:0]
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 0
P0.15 |  | P0.14 |  | P0.13 |  | P0.12 |  | P0.11 |  | P0.10 |  | P0.9 |  | P0.8 |  | P0.7 |  | P0.6 |  | P0.5 |  | P0.4 |  | P0.3 |  | P0.2 |  | P0.1 |  | P0.0 | 
PORT P1 [31:16] | PORT P1 [15:0]
PINSEL3[31:0] | PINSEL2[31:0]
PORT P2 [31:16] | PORT P2 [15:0]
PINSEL5[31:0] | PINSEL4[31:0]
System Control Register – Power, Pin function, mode, clock
Embedded System Design Concepts - A simple approach

## Slide 22: PINSEL Register – To choose Multifunctions of a PIN
Initialize P2.11 –P2.13 as GPIO.
Initialize P0.2 & P0.3 as TXD0 & RXD0
Initialize P4.28 & p4.29 as TXD3 & RXD3
Initialize P1.31 as AD0.5
Initialize P0.21 to P0.22 as GPIOs , P0.23 as AD0.0
System Control Register – Power, Pin function, mode, clock
Embedded System Design Concepts - A simple approach

## Slide 23: PINMODE- Pin mode select register values
The PINMODE registers control the input mode of all ports. This includes the use of the on-chip pull-up/pull-down resistor feature and a special open drain operating mode.
Repeater mode enables the pull-up resistor if the pin is at a logic high and enables the pull-down resistor if the pin is at a logic low. This causes the pin to retain its last known state.
state if it is configured as an input and is not driven externally.
System Control Register – Power, Pin function, mode, clock
PINMODE Register – To choose Multifunction of a PIN
Embedded System Design Concepts - A simple approach

## Slide 24
Let us understands how to use GPIOs are configured to operate in different modes
Push-Pull configuration
Open drain configuration
System Control Register – Power, Pin function, mode, clock
Embedded System Design Concepts - A simple approach

## Slide 25
How Input and Output devices are connected ?
System Control Register – Power, Pin function, mode, clock
Embedded System Design Concepts - A simple approach

## Slide 26
Learning – General Purpose Input and Outputs
Let us understands how to use GPIOs
GPIOs used as Output
4:1
MUX
PINs as Open Drain
PINs Pull Up or Pull down Internal Resistor
Embedded System Design Concepts - A simple approach

## Slide 27
System Control Register – Power, Pin function, mode, clock
PCLKSEL Register – To choose Multifunction of a PIN
Embedded System Design Concepts - A simple approach

## Slide 28
CPU_CLOCK (CCLK) = 72MHz
Peripheral CLK Divider
PCLKSEL0
18M
04
System Control Register – Power, Pin function, mode, clock
PCLKSEL Register – To choose Multifunction of a PIN
Embedded System Design Concepts - A simple approach

## Slide 29
mahesha@pes.edu
+91 9741172822
THANK YOU
Mahesh Awati
Department of Electronics and Communication